## Slide 1: Lesson 9: Tsunami Hazard

## Slide 2: Goal and Objectives
Goal
This lesson will discuss the tsunami hazard and tsunami-specific inventory in Hazus.
After completing this lesson, you will be able to:
  Define tsunami
  Describe near and distant source tsunamis
  Understand tsunami-specific inventory

## Slide 3: Hazus Tsunami Model
  Loss estimation model that provides state-of-the-art decision support software for estimating potential losses from tsunamis.
  Available for 5 Very High-risk states (AK, WA, OR, CA, HI) and the 5 High Risk U.S. territories
  Combined Earthquake/Tsunami analysis functionality available for the 5 states and PR

## Slide 4: Tsunami Overview
A series of long-period waves that are usually generated by an impulsive disturbance that displaces massive amounts of water
  Travels at speeds of > 450 mph across the ocean, slowing as it approaches shallower water
  A series of waves with minutes to hours between the first wave may not be the largest
  Encompass the entire water column in open ocean, with an average surface height of 0.5 m

## Slide 5: Tsunami Overview
Tsunamis can be triggered by
  earthquakes
  volcanic activity
  submarine landslides
  onshore landslides in which large volumes of debris fall into the water
All of these triggers can occur in the United States
Most of the tsunamis (88%) in the Global Historical Tsunami Database were generated by earthquakes or landslides caused by earthquakes

## Slide 6: Tsunami Overview
Mega Tsunamis
  Rare but induce high impacts
  Caused by major slipping along the subduction zones
    2011 Tohoku Tsunami
    2004 Indian Ocean Tsunami
    1960 Chilean Tsunami
    Cascadia Subduction Zone
Credit: NOAA PMEL

## Slide 7: Tsunami - Near vs Distant Source
Near Source (local source)
  Those generated within 100 km of a locality of interest
  Earthquake ground shaking precedes the tsunami
  Earthquake damage possible
  Subsidence (lowering) of coastal area possible
  Lead time a few minutes to an hour
Credit: USGS

## Slide 8: Tsunami - Near vs Distant Source
Distant Source
  Those generated far away (>1,000 km from a locality)
  No ground shaking precedes the tsunami
  Lead time few to several hours

## Slide 9: National Structure Inventory (NSI)
  U.S. Army Corp of Engineers National Structural Inventory point data. Developed with FEMA.
  Creates notional structures, or points, in the developed portion of each census block to represent the numbers and types of buildings that occur based on size, occupancy type, construction materials, etc.

## Slide 10: User Defined Facilities
  Enables user specific datasets to be analyzed through the Hazus methodologies providing more accurate results
  User populated table using Hazus CDMS
  Attributes include:
    Occupancy type
    Earthquake building type
    Design level
    First floor height
    Building replacement cost
    Content replacement cost
    Location of structure

## Slide 11: Review
  How might a tsunami be triggered?
  What is the difference between a near and distant source tsunami?
  Which type of tsunami offers the most warning time?
  Describe the tsunami-specific inventory in Hazus.
  What states/territories are included in the Hazus tsunami model?

## Slide 12: Questions?