## Slide 1: Lesson 3: CDMS Structure

## Slide 2: Goal and Objectives
Goal:
Introduce the Comprehensive Data Management System (CDMS)
After completing Lesson 3, you will be able to:
  Understand CDMS concepts
  Navigate the CDMS menus

## Slide 3: What is CDMS?
CDMS, or Comprehensive Data Management System, is a tool developed by FEMA to support integration of locally developed inventory data into the Hazus loss estimation process.
Primary functions:
  Support transfer of data into and out of the master Hazus state databases
  Provide validation of user supplied data
  Allow users to query inventory information
  Provide a graphic interface for non-SQL users

## Slide 4: What is CDMS?

## Slide 5: What is CDMS?
Supports a variety of methods for managing Hazus data types:
  Site Specific inventory
  Aggregated General Building Stock (GBS)
  Building Specific inventory
  User-Defined Facilities (UDF)

## Slide 6: CDMS Home

## Slide 7: Activity 3.1
The Instructor will explore the CDMS Home screen options:
  Help
  Point to state database location
  Package state databases
  Query statewide data
  Export statewide data

## Slide 8: Help
A compiled CDMS Help file is provided and useful for reviewing concepts and definitions.
  Getting Started Instructions
  Searchable
  Querying, Importing, Exporting, and Updating step-by-step instructions

## Slide 9: Default State Database
  The first time that CDMS runs, the user must specify a default statewide database location on a local drive
  User will need to update by state if updating data for different states
  Be sure to verify that you have read/write access to the data

## Slide 10: Querying Statewide Datasets
CDMS allows users to query existing state data by State, County, Census Tract, or Census Block.

## Slide 11: Export Options
  Delete one or more records*
  Export results to Excel or personal Geodatabase
*This is often a useful step prior to updating the inventory

## Slide 12: Backing Up Data
It is a good practice to export the data of interest BEFORE changing it, so that:
  You can report the differences between the original before and updated after records.
  If something goes wrong, you can always go back to the before snapshot.

## Slide 13: Hazus-ID
  Hazus relates tables based on a unique ID value - either create this or have CDMS do so.
  Unique ID must be data type text and eight (8) characters in length in the form (SSxxxxxx) where SS is the state name abbreviation (Upper Case) and xxxxxx is a sequential number from 000001 to 999999.
  CDMS only matches Hazus-IDs within the same Census Block.

## Slide 14: Census ID
Each record in a table must have a Census tract AND block number:
  Must be full Census ID
  State (2 characters) + County (3 characters) + Tract (6 characters) + Block (4 characters)
    e.g., 180973301021234
  This is CDMS assigned if not provided by user

## Slide 15: Coordinate Information
Existing data frequently needs to be massaged to make it Hazus compatible:
  Transform coordinate system to Geographic WGS 1984
  Convert to CDMS accepted format if in coverage, CAD, etc.

## Slide 16: General CDMS Update Process
1. Select the source data file and destination category
2. Define source data parameters
3. Match fields
4. Categorize data
5. Validation
6. Review results in CDMS repository
7. Transfer to state database

## Slide 17: Source Data Parameters
Specifies:
  Table containing data
  Hazus-ID field
  Coordinate fields (dependent on data type)

## Slide 18: Source Category and Dataset
File name and location, category, and inventory dataset.

## Slide 19: Source To Destination Dataset - Example

## Slide 20: Import Table or Worksheet
  If the import is from a Shapefile, the import table is automatically selected.
  If the import is an MS Access or MS Excel file, the user has to specify the table or worksheet that contains the data.

## Slide 21: Field Matching
  Specifies how fields in your input table are related to fields in the Hazus inventory.
  CDMS auto-matches fields with the same name and characteristics.
  Colors indicate which fields are required or can have defaults auto-assigned.

## Slide 22: Field Matching (cont.)

## Slide 23: Categorizing Data

## Slide 24: Validation
  The validation process confirms that records have valid values, and that fields match correctly.
  A report is generated as soon as an error is found. Validation may take several passes.
  All errors must be corrected before any records are imported into the CDMS Repository.

## Slide 25: Data Review
  Verify that your data has imported into CDMS correctly before proceeding
  You have the option to remove unwanted records

## Slide 26: Transferring Data to State Databases
  CDMS stores all imported data in the Repository until you transfer the results to the state dataset
  Two transfer options:
    Append/Update
    Replace Data

## Slide 27: Editing CDMS vs Study Region
  Updating a statewide database using CDMS is different than updating a study region in Hazus
  Editing a statewide database using CDMS will result in that edit appearing in any study region built using that database

## Slide 28: Review
  Name one of the primary functions of CDMS.
  What are the options available on the CDMS Home screen?
  What are the general steps in the CDMS update process?
  When editing a statewide database using CDMS, where will the edits appear?

## Slide 29: Questions?