## Slide 1: CDMS Site Specific Inventory Updates

## Slide 2: Goal and Objectives
Goal:
Learn to use CDMS to update and maintain Site Specific data.
After completing Lesson 4, you will be able to:
  Use CDMS to review and update Site Specific data by type and region.
  Identify strategies for gathering data that can be used to update Site Specific Inventory.
  Describe issues that apply to Site Specific Inventory updates.

## Slide 3: Site Specific vs General Building Stock
Site Specific
  Provides point locations of buildings
General Building Stock (GBS)
  Aggregated locations

## Slide 4: Site Specific Update Process
  Select source data file and destination category
  Define source data parameters
  Match fields
  Categorize data
  Validation
  Review results in CDMS repository
  Transfer to state database

## Slide 5: Activity 4.1
Student Activity
  CDMS Navigation - Site Specific Inventory Updates

## Slide 6: Site Specific Inventory Types
  Essential Facilities: medical, fire, police, etc.
  High Potential Loss Facilities: dams, nuclear, military
  Transportation Systems: bridges, highways, rail, airports, etc.
  Utility Systems: water, oil, gas, electric, etc.
  Hazardous Material Sites
  User Defined Facility (UDF)
    Only portions of WA, OR, AK come packaged with UDF data
  Advanced Engineering Building Model (AEBM)
*Users are encouraged to develop their own UDF data.

## Slide 7: Site Specific Inventory Sources
Sources:
  Vary by inventory type
  The metadata for each inventory component provides information about its source

## Slide 8: Site Specific - Essential Facilities

## Slide 9: Improving Site Specific Data
The next section will discuss ways to improve Site Specific data.

## Slide 10: Hazus Site Specific Inventory - Discussion
If you wanted to improve the Hazus Site Specific inventory, where might you obtain the following data?
  Essential Facilities (fire, police, EOCs, schools, medical care facilities)
  Utilities
  Transportation Facilities
  High Potential Loss Facilities
Where could you obtain information about homes and businesses?

## Slide 11: Property Assessor Data
  Often available from individual county assessors offices, GIS or land information/planning offices, or in a few cases, a state agency.
  Computer Aided Mass Appraisal (CAMA) data is often an excellent resource for improving Hazus building inventory.
  Some agencies may still charge for and/or restrict use of property data.

## Slide 12: Property Data
Property data often uses appraisals for costing information:
  Building replacement costs often need to be separately calculated.
  Building content costs often need to be separately calculated.
*See Chapter 5 in the Flood Technical Manual for more information.
Occupancy | Content Cost
RES1 to RES6 & COM10 | Cost *0.5
COM1 to COM5, COM8, COM9, IND6, AGR1, REL1, GOV1 and EDU1 | Cost*1.0
COM6, COM7, IND1 to IND5, GOV2 and EDU2 | Cost*1.5

## Slide 13: Property Data Considerations
  Look for the following information in your data:
    Square footage
    Duplicate data entries
    Structural type, age, condition, and height of buildings
  While some Hazard specific information is likely not included (e.g. hurricane specific building type), user can use a system of classifying buildings that will have to be mapped to Hazus building types.
  If users only have location, occupancy and building area, CDMS will add the replacement cost fields.

## Slide 14: Property Data Considerations (cont.)
Other considerations when using your local data:
  Physical property address information vs a billing address.
  Search for non-taxed properties (e.g. government buildings, schools, churches, etc.).
  In agricultural areas, a single property parcel may have multiple buildings with assessments.
  Mobile homes and/or manufactured housing may not be identified as individual structures (personal property).

## Slide 15: Property Data Processing Strategies
The effort required to process property data can vary a lot!
  There are many different types of CAMA software some have simple table structures while others are very complex.
  Hazus requires a very specific data structure and values all in a single input table.
  Consider automating processes.

## Slide 16: Raster Imagery
Pictometry
LIDAR
Aerial Photos
  Inventory
    Changes
    Land use
  Modeling
    Overlay losses

## Slide 17: Ortho and Oblique Photography
Use Google Earth and Bing Maps to verify building stock characteristics at the Census Block level
  Building counts
  Number of stories
  Occupancy
  Roof Type

## Slide 18: Google Streetview / Bing Streetside
  Can be useful in filling out missing structure attributes
  Can help determine attributes such as:
    Number of stories
    First floor elevation
    Occupancy type
    Basement
Example:
  Occupancy = RES1
  Number of Stories = 2
  Basement = no
  First floor = 3 ( 4 steps x 8 inches per step)

## Slide 19: Field Data Collection Methods
Drive-by Surveys
  Wall construction
  Number of stories
  Roof shape and cover
  Garage
  Shutters (unknown impact resistance)
Inspections
  Roof deck
  Roof-wall connection
  Shutters (Verified impact standards)
Pros/Cons
  Larger number of homes to sample
  Rapid data collection
  Cannot collect all desired info
Pros/Cons
  Detailed info
  Less homes sampled per $$

## Slide 20: Expert Assistance
  State and local GIS departments
  Universities
  Private consultants
  Engineers
  Tax Assessors
  Hazus user groups

## Slide 21: EQ and FL Table Values
Users can either populate the EQ and FL tables with default values, or they can enter correct values
  See the CDMS Data Dictionary for valid domains

## Slide 22: Occupancy Classification
  Occupancy class is one of the most critical fields to populate correctly. Damage functions are selected based on this value.
  Occupancies are largely based on SIC codes.
HINT: It is frequently necessary to make decisions about how a local occupancy category applies to a Hazus Occupancy Class.
Hazus Label | Occupancy Class | SIC Codes
RES1 | Single Family | 
RES2 | Mobile Home | 
RES3 | Multi-Family Dwelling | 
RES3A | Duplex | 
RES3B | 3-4 Units | 
RES3C | 5-9 Units | 
RES3D | 10-19 Units | 
RES3E | 20-49 Units | 
RES3F | 50+ Units | 
RES4 | Temporary Lodging | 70
RES5 | Institutional Dormitory | 
RES6 | Nursing Home | 8051, 8052, 8059
COM1 | Retail Trade | 52, 53, 54, 55, 56, 57, 59
COM2 | Wholesale Trade | 42, 50, 51
COM3 | Personal and Repair Services | 72, 75, 76, 83, 88
COM4 | Professional/Technical Services | 40, 41, 44, 45, 46, 47, 49, 61, 62, 63, 64, 65, 67, 73, 78 (except 7832), 81, 87, 89

## Slide 23: Creating a User Defined Facilities (UDF) Database
  Minimum required attributes for a default update are Occupancy and Square Footage.
  CDMS will attribute the rest based on default or derived values.
  A default import process will take longer due to the processing required.
  A more fully derived database can be created with user-provided data and will result in a more accurate database.

## Slide 24: User Defined Inventory Data
Attribute | Description | Why is it needed?
Record Identifier (ID) | A unique identifier for each record. Hazus will create its own primary key (it does not prompt the user for one since there is no guarantee it is unique). Map this identifier to any column that is not used. COMMENT is a good candidate. | Hazus will output all results keyed by the ID it generates on import. If a join to the original data is needed, this attribute will be the only way to link the results to the original data.
Occupancy | Occupancy type per the Hazus classification. Map it to OCCUPANCY. | Analyses are based on the occupancy and/or building type.
Building Type | Building type per the Hazus classification. Map it to BLDGTYPE. | Analyses are based on the occupancy and/or building type.
Design Level | Seismic Design Level. Map to DesignLevel. CDMS default is PC. | To assess lateral strength of structure - for building damage
First Floor Height | Top of finished floor relative to adjacent grade (ft). Map to FirstFloorHt. CDMS default is 1, which represents slab on grade. | To assess content damage
Building Replacement Cost | Cost ($) to replace the building in case of damage. Used by economic loss model. Map it to COST. CDMS will estimate based on RS Means table. | To assess building economic loss
Content Replacement Cost | As above (in Building Replacement Cost) relating to building content. Map to Content Cost. CDMS will estimate based on % of building replacement. | To assess content economic loss
Location | The location of the structure/facility can be supplied as latitude/longitude (in that case, Hazus will create the geospatial points), or directly when the table imported is a feature class. | Hazus needs location of structure to calculate the hazard. Hazus uses the location at import to filter the points that do not fall within the study region (i.e., discarding any point that falls outside the study region).

## Slide 25: Append
Option 1: Append/Update Data
  This option should be used when importing a subset of data into a Hazus state dataset.
  The system will try to match the Hazus-ID to the user-specified ID.
    If a match is found, an update of record will take place.
    If a match is not found, a new record will be added to the state dataset.

## Slide 26: Replace
Option 2: Replace Data
  This option should be used when a total replace of state data is needed.
  This option will remove all features residing in a Hazus state dataset for the selected layer.

## Slide 27: Activities 4.2 and 4.3
  Do EITHER activity 4.2 OR 4.3
  You may elect to do the exercise you did not choose outside of class if you like.

## Slide 28: Activity 4.2
Student Activity
  Update inventory data from county provided records and import data into CDMS and transfer them to the state database using Append

## Slide 29: Activity 4.3
Student Activity
  Update inventory data from county provided records, import data into CDMS and transfer them to the state database using Replace.

## Slide 30: Flood Model
There are Site Specific attributes in the "fl" table that are unique to the flood model.

## Slide 31: Flood Modeled Inventory
Modeled Site Specific Inventory
  User defined facilities
  Essential facilities
  Transportation systems (bridges)
  Utilities

## Slide 32: fl User Defined Facilities
  Useful for analyzing individual structures that are normally modeled only as general building stock inventory.
  You must assign one of the existing specific occupancy classes to each facility. User defined facilities are not appropriate for every type of structure!
  For CDMS: Import format must be a shapefile, Excel spreadsheet, or MS Access/personal geodatabase.
  For Hazus: must be a table within a MS Access/personal geodatabase.

## Slide 33: fl User Defined Facilities (Cont.)
Hazus requires minimal construction design characteristics to select the correct damage curve for damage and loss analysis for each facility:
  Area
  Foundation Type (specifically, basement)
  Number of stories
  First floor elevation
  Specific occupancy

## Slide 34: fl User Defined Facilities (Cont.)
User Defined Facility losses reported by Hazus:
  Building losses and percent damage
  Content losses and percent damage
  Inventory losses and percent damage
  Direct Economic losses

## Slide 35: fl Essential Facilities
All Essential Facilities are analyzed in the flood model:
  Care Facilities
  Fire Stations
  Police Stations
  EOC
  Schools

## Slide 36: fl Essential Facility Attributes
Required Attributes:
  Latitude/Longitude
  Building type
  Design level
  Foundation type
  First floor height
*Other attributes are listed in the CDMS Data Dictionary

## Slide 37: fl Essential Facility Assumptions
  Basements - It is assumed that EFFS, EFS1, and EFS2 facilities do not have basements, and that all other classes do have basements.
  First Floor Elevation - It is assumed that EFE0, EFFS, EFS1, and EFS2 are at grade. All other facilities are assumed 3 feet above grade.
  Number of stories - All EFS1, EFHS, EFMC, EFFS, EFPS, and EFEO are assumed low rise structures, and the EFHM and EFHL are mid-rise structures.
  Damage Functions - Comparable damage functions to General Building Stock are used to determine damage.

## Slide 38: Earthquake Model
There are Site Specific attributes in the "eq" table that are unique to the earthquake model.

## Slide 39: Earthquake Modeled Inventory
Modeled Site Specific Inventory:
  User defined facilities
  Essential facilities
  High potential loss facilities
  Transportation systems
  Utilities

## Slide 40: eq User Defined Facilities
Required attributes for earthquake model UDFs:
  Latitude / longitude
  Specific occupancy
  Building type
  Design level
  Year built

## Slide 41: eq Essential Facilities
All Essential Facilities are analyzed in earthquake model:
  Care Facilities
  Fire Stations
  Police Stations
  EOC
  Schools

## Slide 42: eq Essential Facility Attributes
Required attributes:
  Earthquake building type
  Design level
  Soil type
  Liquefaction susceptibility category
  Landslide susceptibility category
  Number of hospital beds (Care)
  Number of fire trucks (Fire stations)
Other attributes are listed in the CDMS Data Dictionary.
Building type, foundation type, and design level are NOT the same attributes as those used for flood.

## Slide 43: Introduction to AEBM Capabilities
Advanced Engineering Building Module (AEBM) allows site-specific analyses for a portfolio of buildings:
  Ground shaking and ground failure quantification
  Damage state probabilities assessment
  Economic loss computations
  Casualties estimates
Inventory items can be entered individually or imported through CDMS into State or Study Region databases.
Provides building-specific loss estimation tools for use by experienced seismic/structural engineers or users with more detailed inventory available.

## Slide 44: Advanced Engineering Building Module (AEBM)
  User creates an AEBM inventory record and identifies the AEBM Profile for each building of interest.
  These sets of linked inventory and profile data define unique properties for each building of interest.
  AEBM develops an initial profile of building response, damage, and loss parameters based on default Hazus values corresponding to the occupancy class, building type, and seismic design level of the building or group of buildings of interest.
  At a minimum, users must provide these three building characteristics to run the AEBM data.

## Slide 45: AEBM: Choose or Define a Profile
Choose from over 16,000 unique building characteristic profiles
Based upon:
  Occupancy
  Building type
  Design level
Linked to:
  Capacity curves
  Fragility curves
  Socio-economic parameters

## Slide 46: AEBM: Creating a Portfolio
  Location-specific
  Must be linked to a previously created profile
  Input for square footage, number of occupants, and economic values (replacement value, content value, and business income)

## Slide 47: Merits of AEBM
  Can model any desired type or use of a building
  Total flexibility on defining the properties of buildings
  Fastest and most comprehensive way to analyze portfolio of buildings with different characteristics
  Only site-specific inventory option in Hazus that provides both social and economic impacts
  Very powerful tool for estimating the benefits of a given mitigation strategy

## Slide 48: Activity 4.4
Student Activity
  Import User Defined Facilities and AEBM Facilities into CDMS

## Slide 49: Hurricane Model
There are Site Specific attributes in the "hu" table that are unique to the hurricane model.

## Slide 50: Hurricane Modeled Inventory
Modeled Site Specific Inventory:
  Essential facilities
  User defined facilities

## Slide 51: hu Essential Facilities
Required attributes:
  ID - supplied when create new record
  Lat/Long
  Essential Facility Class - default assumed
Optional information for more accuracy:
  Wind building scheme name
  Hurricane building type - (SBT - Appendix A SUM)
  Number of beds - (hospitals only)

## Slide 52: hu User Defined Facility
Required attributes:
  ID - supplied when create new record
  Lat/Long
  Occupancy - default assumed = RES1
Optional information for more accuracy:
  Wind building type - (SBT- Appendix A SUM)
  Wind building scheme name

## Slide 53: hu Building Type
Users may assign a unique Specific Building Type and Wind Building Scheme to each facility record.

## Slide 54: Tsunami Modeled Inventory
  The Tsunami model does not directly usethe aggregated Census Tract or Block GBS data used by other models.
  Essential facilities - At this time, the tsunami loss model capability is not available for essential facilities, however,essential facilities are integrated into the GBS information and can be assessed using the UDFcapability.
  UDFs - Best option where damage is evaluated on a building-by-building basis for this class of structures.

## Slide 55: Review
  What are the supported Site Specific file formats that CDMS can export?
  The two options for transferring Site Specific records from the Repository into Hazus are Replace and Append. When should we use Append? When should we use Replace?
  What is the required Site Specific projection system for the data to be imported into CDMS?
  What considerations need to be made if the FL, EQ, TS and/or HU model values are not provided in the source data?
  User Defined Facilities are a unique type of Site Specific. What makes UDFs unique?

## Slide 56: Questions?