## Slide 1: Lesson 5: Aggregate Inventory Updates

## Slide 2: Goal and Objectives
Goal:
Introduce the method for updating Hazus aggregate inventory using CDMS.
After completing this lesson, you will be able to:
  Export Aggregate data by type
  Export Aggregate data by region
  Replace Aggregate data

## Slide 3: Why Update the Aggregated Data?
  Local governments will most likely have more accurate data about the local characteristics, such as demographics or building data.
  Using this data will lead to better analysis results.

## Slide 4: General Building Stock
The core elements of the General Building Stock in each of the Hazus models are identical:
  Building area (in 1,000 sqft)
  Building count
  Building exposure (in $1,000s)
  Content exposure (in $1,000s)
All are categorized by type and occupancy.
The primary source for updating this information is property tax (CAMA) data as discussed earlier in the course.

## Slide 5: Should I Update?
  Losses derived from GBS inventory are most reliable for regional studies - not small area studies!
  Many Hazus outputs - debris, building los estimates, etc. - are dependent on the GBS inventory.
  Prioritization of updates to GBS inventory should be determined with these facts in mind.

## Slide 6: Demographic Data
Used for the following purposes in Hazus:
  Estimation of social loss (shelter needs) due to displaced households
  Casualties (earthquake model only)
  Estimation of building space (square footage) for certain occupancy classes in the Hazus-provided inventory

## Slide 7: Updating From Aggregated Data
GBS tables can be updated from aggregated data:
  Building counts by Census Block/Tract
  Demographics by Census Block/Tract
  Building area by Census Block/Tract
  Structure exposed by Census Block/Tract
  Exposure content by Census Block/Tract

## Slide 8: Aggregated Data Update Process
  Select the source file to import
  Specify the destination category and table to update
  Specify the table to import
  Field matching
  Validation
  View results
  Transfer to state database

## Slide 9: Activity 5.1
Student Activity
  CDMS Navigation Use CDMS to Update Aggregate Data in the Inventory

## Slide 10: Converting Site Specific to Aggregate
The next section will discuss the process for converting Site Specific data to aggregate form.

## Slide 11: Site To Aggregate Process
  Select file to import
  Specify the destination category and table to update
  Specify input table
  Field matching
  Categorize data
  Validation
  View results
  Transfer to state database
Similar to other imports already covered.
HINT: This option is ideal for users that have building data with necessary structural information.

## Slide 12: Aggregating Building/Parcel Data
General Building Stock may also be updated from "non-aggregated" point data.
  Lesson 4 describes a workflow to sync-up the Hazus aggregate data from Site Specific point data. For example, EDU1 information in the GBS can be updated from Site Specific schools.
  Lesson 5 describes a similar strategy to update the Hazus aggregate data from building inventory. A common source for building inventory is parcel centroids or building footprints (potential building locations) linked to assessor records (building improvements).

## Slide 13: Requirements - Aggregated Data
Imported table must conform to the structure of the state database table you are updating. At minimum you must have:
  Area (square feet)
  Building Value
  Content Value
  Building Type
  Occupancy Class
  Height of the structure OR its Number of Stories
  Age OR Years of Construction OR Building Quality
  Census Tract OR Census Block OR Latitude/Longitude
The rest of the fields will be attributed with Hazus default values if none are provided by the user.

## Slide 14: Field Matching
Field matching differences from Site Specific:
  Required user provided fields
  Fields that can be populated with a default value
  Fields in which only one of two or more fields must be provided (example - building quality, age, or year of construction)
WARNING: If there is any aggregate data already in the CDMS Repository, it is deleted and replaced with the new data.

## Slide 15: Activity 5.2
Student Activity
  Update Aggregate Inventory from Site Specific Data

## Slide 16: Hazard-Specific Inventory Updates
This section will discuss hazard-specific aggregate inventory that can be updated.

## Slide 17: Flood-Specific Inventory
  Considers both full and depreciated value of structures
  Uses General Building types and not detailed structural categories
  Agricultural inventory
  Vehicle inventory

## Slide 18: Flood Specific Inventory: Full vs. Depreciated Replacement Value
Full replacement value = the engineering cost to rebuild a structure
  Not the assessed value, market value, or the retail value of new structures
  Does not include the value of the land
RSMeans full replacement cost models upon which Hazus provided data were derived are based on construction:
  Economy
  Average
  Custom
  Luxury

## Slide 19: Flood Specific Inventory: Agriculture - National Resources Inventory (NRI) Data
  National Resources Inventory generated every 5 years by NRCS
  http://www.nrcs.usda.gov/Technical/NRI
  Data on crop types and crop quantities (bushels)
    Top 20 crops for each NRI Regions
    Does not include livestock
  Only agricultural areas considered: using land use - land cover data, Hazus removes urban areas, wetlands, forests, etc.
  Not available in Alaska and U.S. territories

## Slide 20: Flood Specific Inventory: Agriculture - National Agriculture Statistics Service (NASS)
Users should update the out-of-the-box values provided by Hazus by consulting the NASS website prior to performing an agriculture loss assessment.
http://www.nass.usda.gov/index.asp

## Slide 21: Flood Specific Inventory: Agricultural Updates
Approaches:
  Edit within study region
  Update by County FIPS code in CDMS

## Slide 22: Flood Specific Inventory: Vehicles - Default Inventory
Data developed using standard traffic models for planning
  Based on Census Block floor area by Specific Occupancy (e.g., RES1, COM1)
  Valuation based on average new and used vehicles
  Three "occupancy" classifications: Car, LtTrk (light truck), and HvyTrk (heavy truck)

## Slide 23: Flood Specific Inventory: Vehicles - Default Inventory
  Estimates based in part on typical building square footage to vehicle ratios as used by Metropolitan Planning Organizations (MPO)
  Includes day and night estimates

## Slide 24: Flood Specific Inventory: Vehicles - Modifying the Inventory
Vehicle inventory updates are generally not a high priority
  Possible source MPOs or other agencies that address transportation planning needs
Approaches
  Edit within Study Region (discussed in next lesson)
  Update by census block in CDMS

## Slide 25: Activity 8.1
Student Activity
  Aggregate Inventory from Site Specific Data Scenario

## Slide 26: Review
  What are two types of data that can be used by CDMS to update GBS inventory?
  CDMS requires that the user provide an Occupancy Code for each record. Can we update the GBS if we only have records for a Specific Occupancy Code?

## Slide 27: Questions?