## Slide 1: Lesson 6: Mapping Schemes

## Slide 2: Goal and Objectives
Goal:
Understand how building mapping schemes were created and why they are important.
After completing this lesson, you will be able to:
  Understand the hazard-specific mapping schemes for Flood, Earthquakeand Hurricane
  Modify the General Building Stock Mapping Schemes

## Slide 3: Flood Model Mapping Schemes
The next section of this lesson will address the Flood Model Mapping Scheme requirements.

## Slide 4: General Building Types
The Hazus Flood model relies upon the General Occupancy Mapping Schemes to determine how structures are distributed based upon the type of material from which they were constructed.
  Material types are not involved in damage analysis.

## Slide 5: Key Inventory Elements
Key fields to be populated to model flood damage:
  Foundation type
  First floor elevation
  Pre/Post-FIRM relationships
  General Building Type (GBS analysis only)
  Specific occupancy class
  Census block
  Flood hazard zone
These elements are controlled in the Flood Specific Occupancy Mapping in the GBS.

## Slide 6: Flood Model Mapping Schemes
Modeled distribution of foundation types and first floor heights:
  Models differ for Riverine, Coastal, and Great Lakes census blocks and by region
  Models differ for Pre-FIRM and Post-FIRM structures
Applies only to GBS inventory

## Slide 7: Post-FIRM Distribution Guidelines
Slab-on-Grade: Typically not allowed in SFHA Post-FIRM development. Establish the Post-FIRM distribution to match what is actually occurring in the regulated areas.
Fill: Use when the BFE plus freeboard is less than 2 feet above grade. If the BFE plus freeboard is greater than 2 feet above grade, typical construction practice is to use other foundation types such as crawlspace, piers, solid walls, or piles.
Crawlspaces: Use when the BFE plus freeboard is less than 4 feet above grade. If BFE plus freeboard is greater than 4 feet above grade, typical construction practice is to use other foundation types such as piers, solid walls, or piles.

## Slide 8: Post-FIRM Distribution Guidelines
Basements: Typically not allowed in SFHA Post-FIRM development. Establish the Post-FIRM distribution to match what is actually occurring in the regulated areas.
Piers: Use when the BFE plus freeboard is less than 6 feet above grade. If BFE plus freeboard is greater than 6 feet above grade, typical construction practice is to use other foundation types such as solid walls or piles.
Solid Walls: Use when the BFE plus freeboard is less than 8 feet above grade. If the BFE plus freeboard is greater than 8 feet above grade, typical construction practice is to use piles.
Piles: Use when the BFE plus freeboard is 8 feet or greater above grade.

## Slide 9: Activity 6.1
The Instructor will guide students to:
  View the Flood Specific Occupancy Mapping
  Copy and Modify a new Flood Specific Occupancy Mapping Scheme

## Slide 10: First Floor Elevations
You can modify the assumptions about first floor height if you have reason to do so.

## Slide 11: Regional Variation
The Hazus provided GBS accounts for regional variations in Foundation types and First Floor Heights.

## Slide 12: Earthquake Model Mapping Schemes
The next section of this lesson will address the Earthquake Model Mapping Scheme requirements.

## Slide 13: General Building Types
Earthquake model breaks the building inventory up into 5 General Building Construction Types:
  Wood
  Steel
  Concrete
  Masonry
  Manufactured Housing (Mobile Home)

## Slide 14: Importance of Specific Building Type
  Occupancy, use, or type of facility
  General building type category (hazard independent)
  Earthquake-specific building type

## Slide 15: Earthquake Specific Building Types
  The basic model building types are based on FEMA-178 (FEMA, 1992) building classes.
  Building height subclasses were added to reflect the variation of typical building periods and other design parameters with building height.
  Manufactured homes, which are not included in the FEMA-178 classification, were also added.

## Slide 16: Earthquake Specific Building Types
Subdivide General Building Type by:
  Number of stories
  Engineered / Non-engineered (design level, building quality)
Other implicit critical characteristics:
  Design base shear
  Configuration
  Bracing
  Regional

## Slide 17: Mapping Schemes
Distributes building information into Specific Building Types

## Slide 18: Height Classifications
Low Rise:
  1-3 stories
  (except URM 1-2 stories)
Mid Rise:
  4-7 stories
  (except URM 3+ stories)
High Rise:
  8 stories or more

## Slide 19: Design Level
  Pre-code
  Low Seismic - Code
  Moderate Seismic - Code
  High Seismic - Code
  Low Seismic - Special
  Moderate Seismic - Special
  High Seismic - Special

## Slide 20: Specific Building Type (SBT) Example - W1
Wood, light frame
  Usually residential
  Repetitive framing
  Often "conventional construction"
  Wood, plywood diaphragms
  Plywood, oriented strand board, wood, stucco, plaster, or gypsum board shear walls

## Slide 21: Foundation Type Mapping
Users have the ability to modify the default assumption that no buildings are on deep foundations.

## Slide 22: Required Inventory Information
Occupancy Mapping
  By building type
  By age (year of construction)
  By seismic design level (low, moderate, high, pre-code)
  By quality (inferior, typical, superior)

## Slide 23: Building Classification Limitations
Assumes Average Characteristics
  Overestimates damage for better buildings and underestimates damage for poorer buildings.
Grouped At Centroid of Census Tract
  In large tracts, both soil type and other hazard information changes.
  Distance to event source could vary dramatically

## Slide 24: Building Classification Limitations (cont.)
Atypical buildings are not explicitly modeled:
  Mixed systems
  Unusual configurations
  Undefined systems
These types of buildings can be modeled in the AEBM.

## Slide 25: Activity 6.2
The Instructor will guide students to:
  View the Earthquake General Building Type Mapping Schemes
  Copy and Modify a new Earthquake Specific Building Type Mapping Scheme

## Slide 26: Hurricane Model Mapping Schemes
The next section of this lesson will address the Hurricane Model Mapping Scheme requirements.

## Slide 27: General Building Types
Like the Earthquake model, the Hurricane model also breaks the building inventory up into 5 General Building Construction Types:
  Wood
  Steel
  Concrete
  Masonry
  Manufactured Housing (Mobile Home)

## Slide 28: Specific Building Types (SBTs)
*Unique to hurricane model
Sub categories of General Building Types (example)
  Wood
    Single family homes, 1 story
    Single family homes, 2 story
    Multi-unit housing/hotel/motel, 1 story
    Multi-unit housing/hotel/motel, 2 story
    Multi-unit housing/hotel/motel, 3+ stories
SBT's generally subdivide GBT by
  Number of stories
  Primary usage (residential/commercial)
  Engineered/non-engineered

## Slide 29: Specific Building Type (SBT)
Sample of Specific Building Types. Also available under the View>Classifications menu in a hurricane study region.
General Building Type | Specific Building Type | Specific Building Type Description
WOOD | WSF1 | Single Family Homes, 1 Story - Wood
WOOD | WSF2 | Single Family Homes, 2 or More Stories - Wood
WOOD | WMUH1 | Wood Multi-Unit/Hotel/Motel, 1 Story
WOOD | WMUH2 | Wood Multi-Unit/Hotel/Motel, 2 Stories
WOOD | WMUH3 | Wood Multi-Unit/Hotel/Motel, 3 or More
MASONRY | MSF1 | Single Family Homes, 1 Story - Masonry
MASONRY | MSF2 | Single Family Homes, 2 or More Stories - Mas
MASONRY | MMUH1 | Masonry Multi-Unit/Hotel/Motel, 1 Story
MASONRY | MMUH2 | Masonry Multi-Unit/Hotel/Motel, 2 Stories
MASONRY | MMUH3 | Masonry Multi-Unit/Hotel/Motel, 3 or More
MASONRY | MLRM1 | Low-Rise Mas Strip Mall, Up to 15ft high
MASONRY | MLRM2 | Low-Rise Mas Strip Mall, More than 15ft high
MASONRY | MLRI | Low-Rise Mas Warehouse/Factory, 20ft high
MASONRY | MERBL | Masonry Eng Res Bldgs, 1-2 Stories
MASONRY | MERBM | Masonry Eng Red Bldgs, 3-5 Stories
MASONRY | MERBH | Masonry Eng Res Bldgs, 6 or More Stories

## Slide 30: Hurricane Model Mapping Schemes

## Slide 31: Wind Building Characteristics (WBC)

## Slide 32: Mapping Schemes (cont.) - WBC

## Slide 33: Example - Wood, Single Family
  Usually residential
  Repetitive framing
  Number of Stories
    WSF1
    WSF2

## Slide 34: Example - Masonry, Multi-Unit
Masonry walls
  Reinforced
  Marginally engineered or non-engineered
Typical usage
  Multi-family building (apartments
  Hotels/motels
Number of stories
  MMUH1 - 1 story
  MMUH2 - 2 story
  MMUH3 - 3 stories or more

## Slide 35: Example - Manufactured Homes
5 Categories
Categorized by Department of Housing and Urban Development standard (HUD code)
Category | HUD Code
Pre HUD - built before 1976 | MHPHUD
HUD 76 - built 1976-1994 | MH76HUD
HUD 94 - built 1994 and later | 
Region I | MH94HUD-I
Region II | MH94HUD-II
Region III | MH94HUD-III

## Slide 36: Building Stock Models - 9 Regions
  4 regions in Florida
  4 regions for other 21 states
  1 region in Hawaii
Based on:
  Review of building codes in effect in each area
  2010 census data
  Aerial photos review
  Inspection data in Florida
  Real Estate & tax data samples

## Slide 37: Review
  Flood Specific Mapping Schemes distribute the Foundation Types across Census Blocks for each Occupancy Class. Are the default distributions the same for each Census Block, or different?
  Can a Census Block have more than one Flood Specific Mapping Scheme? What about a Census Tract?
  What is the difference between General Mapping Schemes and Specific Mapping Schemes?
  How can CDMS be used to update the Mapping Schemes?

## Slide 38: Questions?