## Slide 1: Lesson 7: Hazus Study Region Editing

## Slide 2: Goals and Objectives
Goal:
Explore options for editing the databases within a Study Region.
After completing this lesson, you will be able to:
  Edit the Study Region inventory
  Edit the Study Region Mapping Schemes
  Post changes from a Study Region to the Hazus state databases
  Post changes made to the Hazus state databases to a Study Region

## Slide 3: What is a Study Region?
  Population and inventory are defined for whole region.
  Hazard may affect part of region, or whole region.
  No damage assessment is performed outside of the Study Region.

## Slide 4: Study Region Size
Study Region database size has been extended to support larger Study Region geographies and more detailed analysis.
The 10GB limit typically allows multi-hazard analysis for a county, and flood Average Annualized Loss (AAL) analysis for a multi-county area (e.g. watershed based Risk MAP projects).
The full version of Microsoft SQL Server must be used if these limits will be exceeded.

## Slide 5: Study Region Site Specific Edits
There are three main ways that the Site Specific inventory within a Study Region may be updated:
  Option 1 - Database edits
  Option 2 - Import data
  Option 3 - Update using CDMS

## Slide 6: Option 1: Database Edits
Add one record at a time.

## Slide 7: Option 2: Import Data
  Open Site Specific inventory table
  Right-click | Start Editing (EQ/HU models only)
  Right-click | Import Data
  Choose GDB and feature class containing records to be imported.
Note: Only MS Access 2003 / ESRI Personal Geodatabases are supported.

## Slide 8: Option 2: Import Data (Cont.)
5. Map the fields in the Source feature class to the fields in the Target feature class.

## Slide 9: Option 2: Import Data - UDFs
  User Defined Facilities are supported in a Study Region
  These can be imported either through CDMS or through the study region GUI

## Slide 10: Option 3: Update using CDMS

## Slide 11: Aggregate Inventory Updates
The next section of this lesson will discuss options for making aggregate inventory updates.

## Slide 12: Individual Record Updates
Individual records in the GBS can be edited within the Study Region.
In the flood model, you must set the table type to specific occupancy and then you can edit the editable fields.

## Slide 13: Bulk Updates
CDMS can bulk update the Hazus GBS state tables:
  Regional or local updates
  From aggregate data or Site Specific data by occupancy class

## Slide 14: Earthquake Model: Occupancy Mapping
Describes the distribution of structures in each Census Tract based on the construction characteristics.
New Mapping Schemes may be created in a Study Region.

## Slide 15: Flood Model Mapping Schemes
  General Occupancy Mapping: Describes distributions of buildings by construction
  Flood Specific Occupancy Mapping: Describes distributions of foundations
  First Floor Elevations: Describes distribution of first floor elevations by foundation type
  Mapping Schemes may beduplicated and edited tobetter reflect localconditions within oneor more Census Blocks.

## Slide 16: Flood Model: Agricultural Inventory
Only applies to the Flood model
Can be updated through CDMS

## Slide 17: Hurricane Model: General Building Type Mapping
Describes the distribution of structures based on General Building Type.
Options:
  Create new schemes based upon an existing scheme
  Edit user defined schemes
  Import
  Export
Edit scheme descriptions for each occupancy type.
Schemes can be assigned to individual Census Tracts.

## Slide 18: Hurricane Model: Specific Building Type Mapping Distribution
Describes the distribution of structures based on wind Specific Building Type (e.g., WSF1, WSF2).
Options:
  Create new schemes based upon a default scheme
  Edit user defined schemes
  Import
  Export

## Slide 19: Hurricane Model: Wind Building Characteristics Distribution
Allows detailed engineering characteristics of buildings to be defined.
Options:
  View
  Copy
  Edit
  Delete
  Import/Export (how file)
Example of WSF1 building distribution

## Slide 20: Migrating Study Region Data to CDMS
The next section of this lesson will discuss the process for migrating Study Region data to CDMS.

## Slide 21: Process - Step 1
1. Click Import into CDMS Repository from Hazus Study Region
HINT: 'Current State' must be set to the same state in which the Study Region is found.

## Slide 22: Process - Step 2
2. Select the inventory to import into the CDMS Repository.

## Slide 23: Process - Steps 3 and 4
3. CDMS will report the status of each data layer. Successful data layers will be imported to the CDMS Repository.
4. View, Remove or Transfer the inventory from the Repository into the Hazus statewide databases.

## Slide 24: Activity 7.1
Student Activity
  Updating a Study Region from Hazus Inventory

## Slide 25: Activity 7.2
Student Activity
  Updating Hazus Inventory from a Study Region

## Slide 26: Review
This lesson describes some ways that a Hazus user can edit data within a Study Region. CDMS can also be deployed to post Study Region changes back to the Hazus statewide tables.
  What are the benefits to posting edits to a Study Region back to the Hazus statewide tables?
  What are the benefits of posting changes to the Hazus statewide tables back to a Study Region?
  How can a user transfer changes from Hazus into a Study Region?

## Slide 27: Questions?